## Slide 1: Mastering Digital Design
Lecture 2
with SystemVerilog on FPGAs
Slides by John Wickerson

## Slide 2: This lecture
Arithmetic and logical operators in Verilog
Clocked circuits
Shift registers
Converting from binary to binary-coded decimal (BCD)

## Slide 3: Arithmetic and Logical Operators

## Slide 4: Integer Arithmetic
Integer arithmetic without carries:
Integer arithmetic with carry-in and carry-out:
module add32 (
input logic [31:0] a, b,
output logic [31:0] sum
);
assign sum = a + b;
endmodule
module add32_carry (
input logic [31:0] a, b,
input logic cin,
output logic [31:0] sum,
output logic cout
);
assign {cout, sum} = a + b + cin;
endmodule
What is the width of the +-operator?

## Slide 5: Question
Prove mathematically that the addition cannot overflow?
module add32_carry (
input logic [31:0] a, b,
input logic cin,
output logic [31:0] sum,
output logic cout
);
assign {cout, sum} = a + b + cin;
endmodule
module mul_add_32 (
input logic [15:0] a, b, c
output logic [31:0] out,
);
assign out = (a * b) + c;
endmodule
Can this arithmetic overflow?

## Slide 6: Boolean operators
Bitwise operators:

## Slide 7: Boolean operators
Bitwise operators: ~(4'b0101) = {~0,~1,~0,~1}

## Slide 8: Boolean operators
Bitwise operators: ~(4'b0101) = {~0,~1,~0,~1}

## Slide 9: Boolean operators
Bitwise operators: ~(4'b0101) = {~0,~1,~0,~1} = {1,0,1,0}

## Slide 10: Boolean operators
Bitwise operators: ~(4'b0101) = {~0,~1,~0,~1} = {1,0,1,0} = 4'b1010

## Slide 11: Boolean operators
Bitwise operators: ~(4'b0101) = {~0,~1,~0,~1} = {1,0,1,0} = 4'b1010 4'b0101 & 4'b0011 = 4'b0001

## Slide 12: Boolean operators
Bitwise operators: ~(4'b0101) = {~0,~1,~0,~1} = {1,0,1,0} = 4'b1010 4'b0101 & 4'b0011 = 4'b0001

## Slide 13: Boolean operators
Bitwise operators: ~(4'b0101) = {~0,~1,~0,~1} = {1,0,1,0} = 4'b1010 4'b0101 & 4'b0011 = 4'b0001
Logical operators:

## Slide 14: Boolean operators
Bitwise operators: ~(4'b0101) = {~0,~1,~0,~1} = {1,0,1,0} = 4'b1010 4'b0101 & 4'b0011 = 4'b0001
Logical operators: !(4'b0101) = 0

## Slide 15: Boolean operators
Bitwise operators: ~(4'b0101) = {~0,~1,~0,~1} = {1,0,1,0} = 4'b1010 4'b0101 & 4'b0011 = 4'b0001
Logical operators: !(4'b0101) = 0

## Slide 16: Boolean operators
Bitwise operators: ~(4'b0101) = {~0,~1,~0,~1} = {1,0,1,0} = 4'b1010 4'b0101 & 4'b0011 = 4'b0001
Logical operators: !(4'b0101) = 0
Reduction operators:

## Slide 17: Boolean operators
Bitwise operators: ~(4'b0101) = {~0,~1,~0,~1} = {1,0,1,0} = 4'b1010 4'b0101 & 4'b0011 = 4'b0001
Logical operators: !(4'b0101) = 0
Reduction operators: &(4'b0101) = 0 & 1 & 0 & 1

## Slide 18: Boolean operators
Bitwise operators: ~(4'b0101) = {~0,~1,~0,~1} = {1,0,1,0} = 4'b1010 4'b0101 & 4'b0011 = 4'b0001
Logical operators: !(4'b0101) = 0
Reduction operators: &(4'b0101) = 0 & 1 & 0 & 1

## Slide 19: Boolean operators
Bitwise operators: ~(4'b0101) = {~0,~1,~0,~1} = {1,0,1,0} = 4'b1010 4'b0101 & 4'b0011 = 4'b0001
Logical operators: !(4'b0101) = 0
Reduction operators: &(4'b0101) = 0 & 1 & 0 & 1 = 1'b0

## Slide 20: Boolean operators
What is the difference between ~a and !a?

## Slide 21: Incomplete specification
If out is not assigned in an always block, the previous value must be retained.
module maybe_mux_3to1 (
input logic a, b, c,
input logic [1:0] sel,
output logic out
);
always_comb begin
case (sel)
2'b00: out = a;
2'b01: out = b;
2'b10: out = c;
endcase
end
endmodule
Missing assignment – what about sel = 2’b11?

## Slide 22: Incomplete specification
If out is not assigned in an always block, the previous value must be retained (a latch).
module maybe_mux_3to1 (
input logic a, b, c,
input logic [1:0] sel,
output logic out
);
always_comb begin
case (sel)
2'b00: out = a;
2'b01: out = b;
2'b10: out = c;
endcase
end
endmodule

## Slide 23: Incomplete specification
Could fix by preceding with a default assignment...
module maybe_mux_3to1 (
input logic a, b, c,
input logic [1:0] sel,
output logic out
);
always_comb begin
out = 'x;
case (sel)
2'b00: out = a;
2'b01: out = b;
2'b10: out = c;
endcase
end
endmodule

## Slide 24: Incomplete specification
Could fix by preceding with a default assignment... ... or by using a default case.
module maybe_mux_3to1 (
input logic a, b, c,
input logic [1:0] sel,
output logic out
);
always_comb begin
case (sel)
2'b00: out = a;
2'b01: out = b;
2'b10: out = c;
default: out = 'x;
endcase
end
endmodule

## Slide 25: An ALU
A[31:0]
B[31:0]
F[2:0]
R[31:0]
F[2:0] | R
{0,0,0} | A + B
{0,0,1} | A + 1
{0,1,0} | A - B
{0,1,1} | A - 1
{1,0,X} | A * B

## Slide 26: An ALU
32'd1
32'd1
0 1
0 1
A[31:0]
B[31:0]
F[2:0]
F[2:1]
F[0]
-
+
*
00 01 10
R[31:0]
F[2:0] | R
{0,0,0} | A + B
{0,0,1} | A + 1
{0,1,0} | A - B
{0,1,1} | A - 1
{1,0,X} | A * B
w1
w2
w3
w4
w5

## Slide 27: An ALU
32'd1
32'd1
0 1
0 1
A[31:0]
B[31:0]
F[2:0]
F[2:1]
F[0]
-
+
*
00 01 10
R[31:0]
module mul16 (
input logic [15:0] a, b,
output logic [31:0] out
);
assign out = a * b;
endmodule
module sub32 (
input logic [31:0] a, b,
output logic [31:0] out
);
assign out = a - b;
endmodule
module add32 (
input logic [31:0] a, b,
output logic [31:0] out
);
assign out = a + b;
endmodule
module mux32three (
input logic [31:0] a, b, c,
input logic [1:0] sel,
output logic [31:0] out
);
always_comb begin
case (sel)
2'b00: out = a;
2'b01: out = b;
2'b10: out = c;
default: out = 'x;
endcase
end
endmodule
module alu (
input logic [31:0] A, B,
input logic [2:0] F,
output logic [31:0] R
);
logic [31:0] w1, w2, w3, w4, w5;
mux32two amux (…);
mux32two smux (…);
add32 add (…);
sub32 sub (…);
mul16 mul (…);
mux32three res (…);
endmodule
module mux32two (
input logic [31:0] a, b,
input logic sel,
output logic [31:0] out
);
assign out = sel ? b : a;
endmodule
w1
w2
w3
w4
w5

## Slide 28: Question
Prove that the following two computations are identical:
A[7:0] – B[7:0] == A[7:0] + ~B[7:0] + 1’b1
ADVANCED - Prove the following:
A[7:0] + B[7:0] == (A[7:0] & B[7:0]) + (A[7:0] | B[7:0])

## Slide 29: Clocked circuits

## Slide 30: Sequential logic
module comb (
input logic a, b, sel,
output logic out
);
always_comb begin
if (sel) out = a;
else out = b;
end
endmodule
module seq (
input logic a, b, sel, clk,
output logic out
);
always_ff @(posedge clk) begin
if (sel) out <= a;
else out <= b;
end
endmodule

## Slide 31: Flip flop vs latch
Latch:
Flip flop:
D
Q
G
D
clk
Q
D
Q
G
D
Q
clk
Gate

## Slide 32: Defining a flip flop
module dff (d, rst, clk, q);
input d, rst, clk;
output q;
reg q;
always @ (posedge clk)
begin
if (!rst) q <= 1'b0;
else q <= d;
end
endmodule
D
Q
clk
rst
Note that you can have multiple always blocks with the same sensitivity list. They'll be run in parallel, so watch out for races!

## Slide 33: Blocking vs non-blocking assignment
Two different types of procedural assigments:
always_ff @(posedge clk) begin
a = b & c;
b = a + c;
end
always_ff @(posedge clk) begin
a <= b & c;
b <= a + c;
end
Blocking: second statement waits for first to finish.
Uses new value of a
Non-Blocking: statements execute in parallel using old values of a and b.

## Slide 34: Blocking vs non-blocking assignment
D
Q
D
Q
D
Q
in
q1
q2
clk
out
module sr_v1 (
input logic in, clk,
output logic out
);
logic q1, q2;
always_ff @(posedge clk) begin
q1 = in;
q2 = q1;
out = q2;
end
endmodule
module sr_v2 (
input logic in, clk,
output logic out
);
logic q1, q2;
always_ff @(posedge clk) begin
q1 <= in;
q2 <= q1;
out <= q2;
end
endmodule

## Slide 35
module clktick #(
parameter int N_BIT = 16
)(
input logic clkin, enable,
input logic [N_BIT-1:0] N,
output logic tick
);
logic [N_BIT-1:0] count = '0;
always_ff @(posedge clkin) begin
tick <= 1'b0;
if (enable) begin
if (count == '0) begin
tick <= 1'b1;
count <= N;
end else begin
count <= count - 1'b1;
end
end
end
endmodule
A flexible clock tick
Pulse tick every N+1 cycles of clkin

## Slide 36: A flexible clock tick
module clktick #(
parameter int N_BIT = 16
)(
input logic clkin, enable,
input logic [N_BIT-1:0] N,
output logic tick
);
logic [N_BIT-1:0] count = '0;
always_ff @(posedge clkin) begin
tick <= 1'b0;
if (enable) begin
if (count == '0) begin
tick <= 1'b1;
count <= N;
end else begin
count <= count - 1'b1;
end
end
end
endmodule
Two assignments to tick in same block.
Last one wins!

## Slide 37: Cascading counters
By connecting our clock tick module in series with a counter module, we can count milliseconds:

## Slide 38: A clock divider
module clkdiv #(
parameter int K_BIT = 16
)(
input logic clkin, enable,
input logic [K_BIT-1:0] K,
output logic clkout
);
logic [K_BIT-1:0] count = '0;
always_ff @(posedge clkin) begin
if (enable) begin
if (count == '0) begin
clkout <= ~clkout;
count <= K;
end else begin
count <= count - 1'b1;
end
end
end
endmodule
F(clkout) =
F(clkin) / 2*(K+1)

## Slide 39: Shift registers

## Slide 40: A shift register
D
Q
D
Q
D
Q
D
Q
data_in
sreg[1]
sreg[2]
sreg[3]
sreg[4]
data_out
clk
module sreg4 (
output logic data_out,
input logic data_in, clk
);
logic [4:1] sreg = '0;
always_ff @(posedge clk) begin
sreg[4] <= sreg[3];
sreg[3] <= sreg[2];
sreg[2] <= sreg[1];
sreg[1] <= data_in;
end
assign data_out = sreg[4];
endmodule

## Slide 41: A shift register
D
Q
D
Q
D
Q
D
Q
data_in
sreg[1]
sreg[2]
sreg[3]
clk
module sreg4 (
output logic data_out,
input logic data_in, clk
);
logic [4:1] sreg = '0;
always_ff @(posedge clk)
sreg <= {sreg[3:1], data_in};
assign data_out = sreg[4];
endmodule
sreg[4]
data_out

## Slide 42: Linear feedback shift register
D
Q
D
Q
D
Q
D
Q
clk
1
0
0
0

## Slide 43: Linear feedback shift register
D
Q
D
Q
D
Q
D
Q
clk
0
1
0
0

## Slide 44: Linear feedback shift register
D
Q
D
Q
D
Q
D
Q
clk
0
0
1
0

## Slide 45: Linear feedback shift register
D
Q
D
Q
D
Q
D
Q
clk
1
0
0
1

## Slide 46: Linear feedback shift register
D
Q
D
Q
D
Q
D
Q
clk
1
1
0
0

## Slide 47: Linear feedback shift register
D
Q
D
Q
D
Q
D
Q
clk
0
1
1
0

## Slide 48: Linear feedback shift register
D
Q
D
Q
D
Q
D
Q
clk
1
0
1
1

## Slide 49: Linear feedback shift register
D
Q
D
Q
D
Q
D
Q
clk
0
1
0
1

## Slide 50: Linear feedback shift register
D
Q
D
Q
D
Q
D
Q
clk
1
0
1
0

## Slide 51: Linear feedback shift register
D
Q
D
Q
D
Q
D
Q
clk
1
1
0
1

## Slide 52: Linear feedback shift register
D
Q
D
Q
D
Q
D
Q
clk
1
1
1
0

## Slide 53: Linear feedback shift register
D
Q
D
Q
D
Q
D
Q
clk
1
1
1
1

## Slide 54: Linear feedback shift register
D
Q
D
Q
D
Q
D
Q
clk
0
1
1
1

## Slide 55: Linear feedback shift register
D
Q
D
Q
D
Q
D
Q
clk
0
0
1
1

## Slide 56: Linear feedback shift register
D
Q
D
Q
D
Q
D
Q
clk
0
0
0
1

## Slide 57: Linear feedback shift register
D
Q
D
Q
D
Q
D
Q
clk
1
0
0
0
This LFSR corresponds to the polynomial 1 + x3 + x4. Other LSFRs are possible, with different polynomials.
A polynomial over GF(2) where + is XOR

## Slide 58: Linear feedback shift register
module lfsr4 (
output logic [4:1] data_out,
input logic clk
);
logic [4:1] sreg = 4'b0001;
always_ff @(posedge clk)
sreg <= {sreg[3:1], sreg[4] ^ sreg[3]};
assign data_out = sreg;
endmodule

## Slide 59: Binary to BCD

## Slide 60: Binary to BCD
 | binary-coded decimal (BCD) |  |  | 8-bit binary | 
 | hundreds | tens | units |  | 
 |  |  |  | 0111 | 1100
shift: |  |  | 0 | 1111 | 100
shift: |  |  | 01 | 1111 | 00
shift: |  |  | 011 | 1110 | 0
shift: |  |  | 0111 | 1100 | 
add 3: |  |  | 1010 | 1100 | 
shift: |  | 1 | 0101 | 100 | 
add 3: |  | 1 | 1000 | 100 | 
shift: |  | 11 | 0001 | 00 | 
shift: |  | 110 | 0010 | 0 | 
add 3: |  | 1001 | 0010 | 0 | 
shift: | 1 | 0010 | 0100 |  | 
Check digit 5 after each shift

## Slide 61
B[7:0]
adjust
adjust
adjust
0
adjust
adjust
adjust
0
adjust
adjust
adjust
0
adjust
adjust
adjust
0
adjust
adjust
adjust
adjust
adjust
adjust
0
0
0
0
0
0
0
0
0
0
0
adjust
adjust
adjust
BCD[0]
BCD[1]
BCD[2]
0
0
0
0

## Slide 62
B[7:0]
adjust
adjust
adjust
0
adjust
adjust
adjust
0
adjust
adjust
adjust
0
adjust
adjust
adjust
0
adjust
adjust
adjust
adjust
adjust
adjust
0
0
0
0
0
0
0
0
0
0
0
adjust
adjust
adjust
BCD[0]
BCD[1]
BCD[2]
0
0
0
0

## Slide 63
B[7:0]
adjust
adjust
adjust
0
adjust
adjust
adjust
0
adjust
adjust
adjust
0
adjust
adjust
adjust
0
adjust
adjust
adjust
adjust
adjust
adjust
0
0
0
0
0
0
0
0
0
0
0
adjust
adjust
adjust
BCD[0]
BCD[1]
BCD[2]
0
0
0
0

## Slide 64
B[7:0]
0
0
adjust
0
adjust
0
adjust
adjust
adjust
0
0
0
0
adjust
adjust
BCD[0]
BCD[1]
BCD[2]
0
0
0
0

## Slide 65
B[7:0]
adjust
adjust
adjust
adjust
adjust
0
0
0
0
adjust
adjust
BCD[0]
BCD[1]
BCD[2]

## Slide 66
B[7:0]
BCD[0]
BCD[1]
BCD[2]
adjust
adjust
adjust
adjust
adjust
adjust
adjust
0
0
0
0

## Slide 67: Binary to BCD

## Slide 68: This lecture
Arithmetic and logical operators in Verilog
Clocked circuits
Shift registers
Converting from binary to binary-coded decimal (BCD)

## Slide 69: Backup Bin2BCD Proof
1. What each step must compute
Read the binary input from left to right. Appending a bit
b ∈ {0, 1} to a prefix of value V gives
V′ = 2V + b
Example: appending 1 to binary 111 gives binary 1111.
15 = 2 × 7 + 1
Each step must therefore double the current value and add
the next input bit, keeping the result in BCD.

## Slide 70: Backup Bin2BCD Proof
2. Why adding 3 works for one digit
Let d ∈ {0, …, 9} be a decimal digit and c ∈ {0, 1} the incoming
bit: the next input bit for units, or a carry for other digits.
Required: digit = (2d + c) mod 10, carry = ⌊(2d + c) / 10⌋
If d < 5
0 ≤ 2d + c ≤ 9, so a normal shift gives the correct digit
and no carry. No adjustment is needed.
If d ≥ 5
Add 3 before shifting: 2(d + 3) + c = 2d + c + 6.
This lies between 16 and 25, so the 4-bit group carries 1.
The remaining digit is 2d + c + 6 − 16 = 2d + c − 10.
Why 3? (16 − 10) / 2 = 3