## Slide 1: Mastering Digital Design
Lecture 4
with SystemVerilog on FPGAs
Slides by John Wickerson

## Slide 2: This lecture
The design of the spi2dac module
How the ADC works
Wrapping up

## Slide 3: This lecture
The design of the spi2dac module
How the ADC works
Wrapping up

## Slide 4: spi2dac
parameter logic [4:0] TC = 5'd24;
logic [4:0] ctr;
always_ff @(posedge clk_50MHz) begin
if (ctr == 5'd0) begin
ctr <= TC;
clk_1MHz <= ~clk_1MHz;
end else begin
ctr <= ctr - 1'b1;
end
end

## Slide 5: spi2dac
parameter TC = 5'd24;
reg [4:0] ctr;
always @ (posedge clk_50MHz)
if (ctr==0) begin
ctr <= TC;
clk_1MHz <= ~clk_1MHz;
end else ctr <= ctr - 1'b1;

## Slide 6: spi2dac
parameter TC = 5'd24;
reg [4:0] ctr;
always @ (posedge clk_50MHz)
if (ctr==0) begin
ctr <= TC;
clk_1MHz <= ~clk_1MHz;
end else ctr <= ctr - 1'b1;
logic [4:0] state;
always_ff @(posedge clk_1MHz) begin
case (state)
5'd0: begin
if (dac_start == 1'b1)
state <= state + 1'b1;
end
5'd17: state <= 5'd0;
default: state <= state + 1'b1;
endcase
end
always_comb begin
case (state)
5'd0: {dac_cs, dac_ld} = 2'b11;
5'd17: {dac_cs, dac_ld} = 2'b10;
default: {dac_cs, dac_ld} = 2'b01;
endcase
end
parameter logic BUF = 1'b1;
parameter logic nGA = 1'b1;
parameter logic nSHDN = 1'b1;
logic [3:0] cmd;
logic [15:0] sreg;
assign cmd = {1'b0, BUF, nGA, nSHDN};
always_ff @(posedge clk_1MHz) begin
if ({dac_start, dac_cs} == 2'b11)
sreg <= {cmd, data_in, 2'b00};
else
sreg <= {sreg[14:0], 1'b0};
end
assign dac_sck = !clk_1MHz & !dac_cs;
assign dac_sdi = sreg[15];

## Slide 7: This lecture
The design of the spi2dac module
How the ADC works
Wrapping up

## Slide 8: This lecture
The design of the spi2dac module
How the ADC works
Wrapping up

## Slide 9: ADC using SAR
control logic
+
-
sample & hold
DAC
Vin
VDAC
Vref
out
successive
approximation
register
1 | 0 | 0 | 0
8V
9.4V

## Slide 10: ADC using SAR
control logic
+
-
sample & hold
DAC
Vin
VDAC
Vref
out
16V
9.4V
successive
approximation
register
1 | 0 | 0 | 0
8V
9.4V

## Slide 11: ADC using SAR
control logic
+
-
sample & hold
DAC
Vin
VDAC
Vref
out
16V
successive
approximation
register
1 | 1 | 0 | 0
12V
9.4V

## Slide 12: ADC using SAR
control logic
+
-
sample & hold
DAC
Vin
VDAC
Vref
out
16V
successive
approximation
register
1 | 0 | 1 | 0
10V
9.4V

## Slide 13: ADC using SAR
control logic
+
-
sample & hold
DAC
Vin
VDAC
Vref
out
16V
successive
approximation
register
1 | 0 | 0 | 1
9V
9.4V

## Slide 14: ADC using SAR
control logic
+
-
sample & hold
DAC
Vin
VDAC
Vref
out
16V
successive
approximation
register
1 | 0 | 0 | 1
9V
9.4V

## Slide 15: ADC using SAR
control logic
+
-
sample & hold
DAC
Vin
VDAC
Vref
out
16V
successive
approximation
register
1 | 0 | 0 | 0
8V
5.5V
5.5V

## Slide 16: ADC using SAR
control logic
+
-
sample & hold
DAC
Vin
VDAC
Vref
out
16V
successive
approximation
register
0 | 1 | 0 | 0
4V
5.5V
5.5V

## Slide 17: ADC using SAR
control logic
+
-
sample & hold
DAC
Vin
VDAC
Vref
out
16V
successive
approximation
register
0 | 1 | 1 | 0
6V
5.5V
5.5V

## Slide 18: ADC using SAR
control logic
+
-
sample & hold
DAC
Vin
VDAC
Vref
out
16V
successive
approximation
register
0 | 1 | 0 | 1
5V
5.5V
5.5V

## Slide 19: ADC using SAR
control logic
+
-
sample & hold
DAC
Vin
VDAC
Vref
out
16V
successive
approximation
register
0 | 1 | 0 | 1
5V
5.5V
5.5V

## Slide 20: ADC using SAR
An N-bit ADC takes N cycles to convert one sample
Low power consumption
Simple design with small circuit area
Low latency
More advanced designs are more efficient when the sampling rate is above 10MHz or N > 16.

## Slide 21: This lecture
The design of the spi2dac module
How the ADC works
Wrapping up

## Slide 22: Module aims
To ensure that all MSc students reach a common competence level in RTL design using FPGAs in a hardware description language.
To act as a revision exercise for those already competent in Verilog and FPGAs.

## Slide 23: Grading
This lab is part of the Coursework component of the MSc course.
You must pass this component, but it does not count towards your final MSc grade.
Coursework
Exams
Project
This lab

## Slide 24: Assessment
Assessment will be via a 15-minute oral interview. This will assess:
  how many parts of the experiment you have completed,
  the extent to which you have understood the underlying principles of digital design, and
  whether you have used a logbook (electronic or paper) to help you learn through planning and reflection.
Please have your equipment set up and ready to demo.

## Slide 25: Admin
Final two labs: Tuesday 9th & 16th Nov at 0900–1200.
Vivas: how about in the week beginning Monday 22nd Nov?