## Slide 1: Mastering Digital Design
Lecture 1
with Verilog on FPGAs
Slides by John Wickerson

## Slide 2: Before we start
Please ask questions during lectures
If you can’t understand me – say something I will enunciate
AI usage
Maths
RTL
EDA Research

## Slide 3: Module aims
To ensure that all MSc students reach a common competence level in RTL design using FPGAs in a hardware description language.
To act as a revision exercise for those already competent in SystemVerilog and FPGAs.

## Slide 4: Format
The lab experiment is divided into four parts.
It is hoped that you will finish one part each week.
Each part has clearly defined Learning Outcomes.
These lectures will supplement the lab with some background information.

## Slide 5: Grading
This lab is part of the Coursework component of the MSc course.
You must pass this component, but it does not count towards your final MSc grade.
Coursework
Exams
Project
This lab

## Slide 6: Assessment
Assessment will be via a short oral interview. This will assess:
  how many parts of the experiment you have completed,
  the extent to which you have understood the underlying principles of digital design, and
  whether you have used a logbook (electronic or paper) to help you learn through planning and reflection.
Please have your equipment set up and ready to demo.

## Slide 7: Admin
Lectures (1hr): Mondays at 14:00–15:00
  5th, 19th, 26th October & 2nd November
Labs (3 hrs): Tuesday at 9:00 – 12:00
  6th, 20th, 27th October & 3rd November
Assessment: Tuesday 10th November at 9:00 to 11:00
Course webpage: https://github.com/Mastering-Digital-Design/Lab-Module

## Slide 8: Labs – by tomorrow!!
Pair up – and tell me who is paired up
Visit Level 1 Stores and collect the following:
  DE1-SoC board
  Analogue I/O extension board (PKYC v1.0)
  Wired earphones (if you don’t have your own)

## Slide 9: To do
Group yourselves into pairs.
Record who is in your pair in the spreadsheet on Teams.
Collect a DE1-SoC board from Stores (Level 1 of the EEE building), one per pair. You'll need to have your college card with you.
Do the exercises, with support from the GTAs on ??? mornings, and keep a logbook along the way.
Come (as a pair) to your 15-minute viva (with your logbook) near the end of this term.

## Slide 10: Credits
This course was conceived and designed by Professor Peter Cheung.
Any errors in the lectures are mine. (And please do let me know if you find any!)

## Slide 11: Digital Design

## Slide 12: The old days
Discrete logic, built from individual gates or packages containing small digital building blocks (e.g. a 1-bit adder).
Thanks to De Morgan, we can build anything using 2-input NAND gates!
But this is tedious, expensive, and prone to wiring errors.

## Slide 13: Early integrated circuits
Rows of gates, connected to form application-specific integrated circuits (ASICs).
Can be full-custom (fabricated from scratch), or semi-custom (can only adjust the wiring between rows).
Functionality cannot be later changed.

## Slide 14: Full-custom ICs
Here is an Apple A12 processor from the iPhone XS. It has about 6.9 billion transistors.
Very expensive to design and manufacture, so not viable unless the market is very large.
https://www.techinsights.com/blog/apple-iphone-xs-max-teardown
~9mm

## Slide 15: Field-programmable gate arrays (FPGAs)
Introduced by Xilinx (now part of AMD) in 1985.
Other manufacturers include Altera, Microsemi (now part of Microchip), and Lattice.
Arrays of programmable logic blocks, programmable wiring in between, and flexible I/O.
logic block
I/O pad
switch block

## Slide 16: Logic blocks
Also called logic elements.
Based around look-up tables (LUTs), usually with 4 inputs.
Optional flipflop (FF) at the output.
These can implement any 4-input Boolean function (truth table).
LUT
FF
A
B
C
D
reset
clock
out

## Slide 17: Multiplexer (MUX)
MUX
in3
in1
in2
out

## Slide 18: Logic blocks
MUX
MUX
MUX
MUX
MUX
MUX
MUX
MUX
0
1
1
0
0
0
1
1
0
1
1
1
1
0
0
1
MUX
MUX
MUX
MUX
MUX
MUX
MUX
D
C
B
A
X
A | B | C | D | X
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1
4-LUT

## Slide 19: Field-programmable gate arrays (FPGAs)
logic block
I/O pad
switch block
Introduced by Xilinx (now part of AMD) in 1985.
Other manufacturers include Altera, and Lattice.
Arrays of programmable logic blocks, programmable wiring in between, and flexible I/O.

## Slide 20: Programmable routing
0
1
1
0
0
0

## Slide 21: Programmable routing
0
1
1
0
0
0

## Slide 22: Question?
A
B
X
Y
Draw Your Circuit Here?
C D
1. Can you draw a circuit using MUX’s, so that I can output any of the following four combinations?
X,Y = {A,A}, {A,B}, {B,A}, {B,B}
2. What if I remove D?

## Slide 23: Configuring an FPGA
All these configuration registers are set by passing the FPGA a configuration bitstream.
Powering up the board puts the FPGA chip into a "waiting" mode (LEDs flashing). You then send the board the bitstream of your design via the USB port.

## Slide 24: Cyclone V FPGA
The Altera Cyclone V FPGA uses a more complex FPGA logic blocks called Adaptive Logic Modules (ALMs).
The device we use (5CSEMA5F31C6N) has 32000 ALMs. That's roughly equivalent to 85000 4-LUTs, or about 2000 32-bit binary adders.
Not that this particularly matters for FPGA users.

## Slide 25: Cyclone V FPGA
The Cyclone V also has 4MB of embedded memory, 87 DSP blocks (for multiply-accumulate), a 2-core ARM processor, and hard logic for interfacing with PCIe and external memory.

## Slide 26: The DE1-SoC board
Everything you need to test basic designs involving switches, 7-segment displays, and even VGA output.

## Slide 27: Add-on board
Provides analogue inputs (from microphone) and outputs (to headphone jack).
Will feature in the third and fourth parts of the lab – you can ignore it for now.

## Slide 28: Design Tools
We use Altera Quartus II to design for FPGA.
Features include: design entry, compilation from HDL, synthesis, simulation, timing analysis, power analysis, project management.
The software is installed on all the PCs in the department.

## Slide 29: SystemVerilog

## Slide 30: SystemVerilog
A hardware description language based on C syntax.
An extension of Verilog (early 2000’s) – types + verification
Description can be at behavioural level, register-transfer level (RTL), or gate level.
Closest competitor, VHDL.
Other HDLs include Chisel and Bluespec.

## Slide 31: Schematic vs HDL
Schematics:
Provide overview
Direct connection to hardware
No programming needed
HDL:
Flexible and parameterisable
Simple textual format
Connection to high-level languages

## Slide 32: SystemVerilog modules
A SystemVerilog design consists of many interconnected modules.
A module contains computations, assignments, and other modules.
a | b | sel | out | outbar
0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0
0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0
// Function: 2-to-1 multiplexer
module mux2to1 (
output logic out, outbar,
input logic a, b, sel
);
assign out = sel ? a : b;
assign outbar = ~out;
endmodule

## Slide 33: Verilog syntax
// Function: 2-to-1 multiplexer
module mux2to1 (
output logic out, outbar,
input logic a, b, sel
);
assign out = sel ? a : b;
assign outbar = ~out;
endmodule
Specify port as input/output/inout
Express module's behaviour. Each statement executes in parallel. Order doesn't matter.
Declare module, list its ports, terminate with ;
Comments can also use /* ... */
Other operators include: &, |, +, -, *
This is continuous assignment. Output responds to changes in input immediately.

## Slide 34: Gate-level description
Built-in logic gates include: and, nand, or, nor, xor, xnor, not, buf.
a1
a2
o1
i1
i2
In practice, "gate-level description" depends on what primitives are provided by your target chip.
// Function: 2-to-1 multiplexer as gates
module mux_gate (
input logic a, b, sel,
output logic out, outbar
);
logic out1, out2, selb;
not i1 (selb, sel);
and a1 (out1, a, sel);
and a2 (out2, b, selb);
or o1 (out, out1, out2);
not i2 (outbar, out);
endmodule

## Slide 35: Combinational blocks
module mux2to1 (
input logic a, b, sel,
output logic out, outbar
);
always_comb begin
if (sel) out = a;
else out = b;
outbar = ~out;
end
endmodule
always_comb blocks define combinational logic – no “state”
Blocking assignments (=)
Statements run in order
Incomplete assignments leads to unintended latch
Can also contain case and for
Automatic sensitivity list

## Slide 36: always_comb blocks
Can mix procedural and continuous assignments.
module mux2to1 (
input logic a, b, sel,
output logic out, outbar
);
always_comb begin
if (sel) out = a;
else out = b;
outbar = ~out;
end
endmodule
module mux2to1 (
input logic a, b, sel,
output logic out, outbar
);
always_comb begin
if (sel) out = a;
else out = b;
end
assign outbar = ~out;
endmodule

## Slide 37: Numerical constants
Format is <size>'<signedness><base><number>
<size> defaults to 32.
<base> is either b (binary=2), o (octal=8), d (decimal=10), or h (hexadecimal=16). Decimal is the default.
<signedness> is either blank (unsigned, default) or s (signed).
Examples: 2'b10, 'b10, 31, 8'hAf, 2'sb10
logic [7:0] zeros = '0; // 00000000
logic [7:0] ones = '1; // 11111111

## Slide 38: Aside: signed numbers
8 | 4 | 2 | 1 | value
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 2
0 | 0 | 1 | 1 | 3
0 | 1 | 0 | 0 | 4
0 | 1 | 0 | 1 | 5
0 | 1 | 1 | 0 | 6
0 | 1 | 1 | 1 | 7
1 | 0 | 0 | 0 | 8
1 | 0 | 0 | 1 | 9
1 | 0 | 1 | 0 | 10
1 | 0 | 1 | 1 | 11
1 | 1 | 0 | 0 | 12
1 | 1 | 0 | 1 | 13
1 | 1 | 1 | 0 | 14
1 | 1 | 1 | 1 | 15
4-bit unsigned:
s | 4 | 2 | 1 | value
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 2
0 | 0 | 1 | 1 | 3
0 | 1 | 0 | 0 | 4
0 | 1 | 0 | 1 | 5
0 | 1 | 1 | 0 | 6
0 | 1 | 1 | 1 | 7
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | -1
1 | 0 | 1 | 0 | -2
1 | 0 | 1 | 1 | -3
1 | 1 | 0 | 0 | -4
1 | 1 | 0 | 1 | -5
1 | 1 | 1 | 0 | -6
1 | 1 | 1 | 1 | -7
sign + 3-bit unsigned:
-8 | 4 | 2 | 1 | value
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 2
0 | 0 | 1 | 1 | 3
0 | 1 | 0 | 0 | 4
0 | 1 | 0 | 1 | 5
0 | 1 | 1 | 0 | 6
0 | 1 | 1 | 1 | 7
1 | 0 | 0 | 0 | -8
1 | 0 | 0 | 1 | -7
1 | 0 | 1 | 0 | -6
1 | 0 | 1 | 1 | -5
1 | 1 | 0 | 0 | -4
1 | 1 | 0 | 1 | -3
1 | 1 | 1 | 0 | -2
1 | 1 | 1 | 1 | -1
4-bit 2's complement:

## Slide 39: Question?
s | 4 | 2 | 1 | value
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 2
0 | 0 | 1 | 1 | 3
0 | 1 | 0 | 0 | 4
0 | 1 | 0 | 1 | 5
0 | 1 | 1 | 0 | 6
0 | 1 | 1 | 1 | 7
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | -1
1 | 0 | 1 | 0 | -2
1 | 0 | 1 | 1 | -3
1 | 1 | 0 | 0 | -4
1 | 1 | 0 | 1 | -5
1 | 1 | 1 | 0 | -6
1 | 1 | 1 | 1 | -7
sign + 3-bit unsigned:
-8 | 4 | 2 | 1 | value
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 2
0 | 0 | 1 | 1 | 3
0 | 1 | 0 | 0 | 4
0 | 1 | 0 | 1 | 5
0 | 1 | 1 | 0 | 6
0 | 1 | 1 | 1 | 7
1 | 0 | 0 | 0 | -8
1 | 0 | 0 | 1 | -7
1 | 0 | 1 | 0 | -6
1 | 0 | 1 | 1 | -5
1 | 1 | 0 | 0 | -4
1 | 1 | 0 | 1 | -3
1 | 1 | 1 | 0 | -2
1 | 1 | 1 | 1 | -1
4-bit 2's complement:
Why do we usually prefer 2’s complement?
Why can’t we represent +8?

## Slide 40: Buses
Concatenate wires into a bus using {...} syntax. E.g.: input logic [15:0] x; output logic [15:0] y; assign y = { x[7:0], x[15:8] };
An 8-bit multiplexer:
module mux2to1 (
input logic [7:0] a, b,
input logic sel,
output logic [7:0] out, outbar
);
always_comb begin
if (sel) out = a;
else out = b;
end
assign outbar = ~out;
endmodule

## Slide 41: Case statements
always_comb begin
if (sel) out = a;
else out = b;
end
always_comb begin
case (sel)
1'b0: out = b;
1'b1: out = a;
endcase
end

## Slide 42: Putting it all together

## Slide 43: 7-seg decoder

## Slide 44: 7-seg decoder

## Slide 45: First attempt
Draw a schematic:

## Slide 46: Second attempt
Gate-level description:
and AND1 (A, ~in[3], ~in[2] ~in[1]);
and AND2 (B, ~in[3], in[2], in[1], in[0]);
and AND3 (C, in[3], in[2], ~in[1], ~in[0]);
or OR1 (out[6], A, B, C);

## Slide 47: Third attempt
Use continuous assignment:
and AND1 (A, ~in[3], ~in[2] ~in[1]);
and AND2 (B, ~in[3], in[2], in[1], in[0]);
and AND3 (C, in[3], in[2], ~in[1], ~in[0]);
or OR1 (out[6], A, B, C);
assign out[6] = (~in[3] & ~in[2] & ~in[1])
| (~in[3] & in[2] & in[1] & in[0])
| ( in[3] & in[2] & ~in[1] & ~in[0]);

## Slide 49: Fourth attempt

## Slide 50: SystemVerilog to FPGA
Elaboration: check syntax, instantiate modules etc
Synthesis: map to gates, logic optimisation, infer registers, much more…
Place & Route: fix gate locations and wire them up, assign to FPGA-specific blocks
Assembler: produce bitpattern to configure the FPGA
Technology Mapping
AND/OR/XOR
LUTs/DSPs

## Slide 51: Lab groups