## Slide 1: Mastering Digital Design
Lecture 3
with SystemVerilog on FPGAs
Slides by John Wickerson

## Slide 2: This lecture
Pulse-width modulation (PWM)
Finite state machines (FSMs)
The analogue add-on card

## Slide 3: This lecture
Pulse-width modulation (PWM)
Finite state machines (FSMs)
The analogue add-on card

## Slide 4: DAC
Digital-to-analogue conversion (DAC) can be done using a string of resistors.
R
R
R
R
R
R
R
R
sw7
sw6
sw5
sw4
sw3
sw2
sw1
sw0
Vref
VDAC
output
buffer
A 3-bit DAC uses 23 = 8 resistors.
When the digital input is 5, we close (only) switch sw5, which means VDAC is ⅝Vref.
Resistors in series:

## Slide 5: DAC
R
R
R
R
R
R
R
R
sw7
sw6
sw5
sw4
sw3
sw2
sw1
sw0
Vref
VDAC
output
buffer
MUX
MUX
MUX
MUX
MUX
MUX
MUX
in[1]
in[2]
in[0]
1
1
0
1
0
1
0
1
0
1
0
1
0
1
0

## Slide 6: DAC via PWM
DAC can also be done using digital components, via pulse-width modulation (PWM).
counter (sawtooth)
data in
PWM signal
+ low pass filter

## Slide 7
DAC can also be done using digital components, via pulse-width modulation (PWM).
DAC via PWM

## Slide 8: DAC via PWM
module pwm (
input logic clk,
input logic [9:0] data_in,
input logic load,
output logic pwm_out
);
logic [9:0] d = '0;
logic [9:0] count = '0;
always_ff @(posedge clk)
if (load == 1’b1) d <= data_in;
always_ff @(posedge clk) begin
count <= count + 1'b1;
if (count > d)
pwm_out <= 1'b0;
else
pwm_out <= 1'b1;
end
endmodule

## Slide 9: This lecture
Pulse-width modulation (PWM)
Finite state machines (FSMs)
The analogue add-on card

## Slide 10: This lecture
Pulse-width modulation (PWM)
Finite state machines (FSMs)
The analogue add-on card

## Slide 11: Example 1: denoiser
Task:
state | meaning | output
a | "definitely low" | 0
b | "maybe rising" | 0
c | "definitely high" | 1
d | "maybe falling" | 1
0
1
0
1
0
1
1

## Slide 12: Mealy machines
next state
current state
input
output
combinational logic
state
register
combinational logic

## Slide 13: Moore machines
next state
current state
input
output
combinational logic
state
register
combinational logic

## Slide 14: Mealy vs Moore
Mealy machines are a bit more complicated to design.
Moore machines tend to require more states.
Outputs of Moore machines are delayed.
Question: What kind of machine did we just describe for the denoiser?

## Slide 15: Implementing the FSM
state | meaning | output
a | "definitely low" | 0
b | "maybe rising" | 0
c | "definitely high" | 1
d | "maybe falling" | 1

## Slide 16: Implementing the FSM
state | meaning | output
00 | "definitely low" | 0
01 | "maybe rising" | 0
11 | "definitely high" | 1
10 | "maybe falling" | 1
Try to make the output value and the state number similar.
Try to change one bit of the state number per transition.
If two parts of the FSM have identical transitions, try to give the corresponding states similar numbers

## Slide 17: Implementing the FSM
state s[1:0] | meaning | output out | inputin | next state ns[1:0]
00 | "definitely low" | 0 | 0 | 00
 |  |  | 1 | 01
01 | "maybe rising" | 0 | 0 | 00
 |  |  | 1 | 11
11 | "definitely high" | 1 | 0 | 10
 |  |  | 1 | 11
10 | "maybe falling" | 1 | 0 | 00
 |  |  | 1 | 11

## Slide 18: Implementing the FSM
state s[1:0] | meaning | output out | inputin | next state ns[1:0]
00 | "definitely low" | 0 | 0 | 00
 |  |  | 1 | 01
01 | "maybe rising" | 0 | 0 | 00
 |  |  | 1 | 11
11 | "definitely high" | 1 | 0 | 10
 |  |  | 1 | 11
10 | "maybe falling" | 1 | 0 | 00
 |  |  | 1 | 11
assign out = s[1];
ns[1] | in=0 | in=1
s=00 | 0 | 0
s=01 | 0 | 1
s=11 | 1 | 1
s=10 | 0 | 1
assign ns[1] = s[1] & s[0] | in & (s[0] | s[1]);

## Slide 19: Implementing the FSM
state s[1:0] | meaning | output out | inputin | next state ns[1:0]
00 | "definitely low" | 0 | 0 | 00
 |  |  | 1 | 01
01 | "maybe rising" | 0 | 0 | 00
 |  |  | 1 | 11
11 | "definitely high" | 1 | 0 | 10
 |  |  | 1 | 11
10 | "maybe falling" | 1 | 0 | 00
 |  |  | 1 | 11
assign out = s[1];
ns[0] | in=0 | in=1
s=00 | 0 | 1
s=01 | 0 | 1
s=11 | 0 | 1
s=10 | 0 | 1
assign ns[1] = s[1] & s[0] | in & (s[0] | s[1]);
assign ns[0] = in;

## Slide 20
state s[1:0] | meaning | output out | inputin | next state ns[1:0]
00 | "definitely low" | 0 | 0 | 00
 |  |  | 1 | 01
01 | "maybe rising" | 0 | 0 | 00
 |  |  | 1 | 11
11 | "definitely high" | 1 | 0 | 10
 |  |  | 1 | 11
10 | "maybe falling" | 1 | 0 | 00
 |  |  | 1 | 11
assign out = s[1];
ns[0] | in=0 | in=1
s=00 | 0 | 1
s=01 | 0 | 1
s=11 | 0 | 1
s=10 | 0 | 1
assign ns[1] = s[1] & s[0] | in & (s[0] | s[1]);
assign ns[0] = in;

## Slide 21: One-hot encoding
"One-hot" means "exactly one bit of a binary number is 1".
One-hot encoding uses more bits, but can lead to simpler logic.
Exercise. Re-implement the FSM using one-hot encoding. Is the logic simpler?
state | encoding as a binary number | one-hot encoding
a | 00 | 0001
b | 01 | 0010
c | 11 | 0100
d | 10 | 1000

## Slide 22: Automated FSM Design
We usually design FSMs at a higher level of abstraction.
module denoiser (
output logic out,
input logic in, clk, rst
);
typedef enum logic [3:0] {
sA = 4'b0001,
sB = 4'b0010,
sC = 4'b0100,
sD = 4'b1000
} state_t;
state_t s = sA;
always_ff @(posedge clk) begin
if (rst) s <= sA;
else begin
case (s)
sA: if (in) s <= sB
sB: if (in) s <= sC;
else s <= sA;
sC: if (!in) s <= sD;
sD: if (in) s <= sC;
else s <= sA;
default: s <= sA;
endcase
end
end
always_comb begin
case (s)
sC, sD: out = 1'b1;
default: out = 1'b0;
endcase
end
endmodule
declare
states
calculate
next state
calculate output

## Slide 23: Question
State | Output | input | Next state in = 1
A | 0 | 0 | B
 |  | 1 | C
B | 0 | 0 | E
 |  | 1 | A
C | 0 | 0 | D
 |  | 1 | C
D | 0 | 0 | E
 |  | 1 | A
E | 1 | 0 | E
 |  | 1 | A
Draw the corresponding FSM?
Can you simplify it and merge some states together?
Notes: The simplified FSM has 3 states (A/C, B/D, E) and detects if we’ve seen two trailing zeros

## Slide 24: Example 2: pulser
Task: Whenever the input rises, output a 1-cycle pulse.

## Slide 25: Example 2: pulser
module pulser (
output logic out,
input logic in, clk
);
typedef enum logic [1:0] {
sIDLE = 2'b00,
sHIGH = 2'b01,
sWAIT = 2'b10
} state_t;
state_t s = sIDLE;
always_ff @(posedge clk) begin
case (s)
sIDLE: if (in) s <= sHIGH;
sHIGH: if (in) s <= sWAIT;
else s <= sIDLE;
sWAIT: if (!in) s <= sIDLE;
endcase
end
always_comb begin
case (s)
sHIGH: out = 1'b1;
default: out = 1'b0;
endcase
end
endmodule
declare
states
calculate
next state
calculate output

## Slide 26: Example 3: delayer
Task: when the 'trigger' input rises, wait for n cycles, then produce a 1-cycle pulse.
Assume n>0

## Slide 27
module delayer (
output logic out,
input logic in,
input logic [9:0] n,
input logic clk
);
typedef enum logic [1:0] {
sIDLE = 2'b00,
sDELA = 2'b01,
sHIGH = 2'b11,
sWAIT = 2'b10
} state_t;
state_t s = sIDLE;
logic [9:0] c = '0;
always_ff @(posedge clk) begin
case (s)
sIDLE: if (in) begin
if (n == '0) s <= sHIGH;
else begin
c <= n - 1'b1;
s <= sDELA;
end
end
sDELA: if (c == '0) s <= sHIGH;
else c <= c - 1'b1;
sHIGH: if (in) s <= sWAIT;
else s <= sIDLE;
sWAIT: if (!in) s <= sIDLE;
default: s <= sIDLE;
endcase
end
always_comb begin
case (s)
sHIGH: out = 1'b1;
default: out = 1'b0;
endcase
end
endmodule

## Slide 28: This lecture
Pulse-width modulation (PWM)
Finite state machines (FSMs)
The analogue add-on card

## Slide 29: This lecture
Pulse-width modulation (PWM)
Finite state machines (FSMs)
The analogue add-on card

## Slide 30: The analogue I/O card
Provides analogue inputs and outputs.
Contains an ADC, a DAC, a low-pass filter, and an op-amp (amplify/buffer a signal).
Will be used for parts 3 and 4 of the experiment.

## Slide 31: Schematic

## Slide 32: Series Peripheral Interface for DAC
To send a value to the DAC, 16 bits are transmitted serially.
Chip select (CS) going low means the start of transmission.
Then serial data in (SDI) takes the following sequence of values.
bit | name | interpretation
15 |  | always 0
14 | BUF | whether Vref is buffered
13 | ¬GA | high = 1x gain, low = 2x gain
12 | ¬SHDN | high = normal, low = shutdown
11–2 |  | the 10 bits of actual data
1–0 |  | these are ignored

## Slide 33: spi2dac
More on this circuit next week!